## Slide 1
UrbanEcho
Noise monitoring for
residential communities
Working local prototype
9 October 2026
Notes: UrbanEcho working local prototype for residential community management. Planning date: 9 October 2026.

## Slide 2
A shared record for community managers
02
INTENDED USER
The manager of a residential society or gated community
A residents’ association or property manager would sponsor an initial pilot.
PROPOSED USE CASE
Review recurring noise near shared areas using location, time and saved incident history.
Pilot question
Does a common record help staff respond sooner and close complaints with clearer evidence?
Notes: Planning hypothesis, not validated customer research. See BUSINESS-CASE.md for buyer, pilot metrics and adoption assumptions. UrbanEcho cannot establish who caused a sound or prove regulatory compliance.

## Slide 3
The working application
03
A map connects each reading to its registered location.
Latest levels and device freshness
Saved incidents and notifications
Location history and daily reports
Three simulated devices report. Older demo devices remain silent, so missing-data indicators stay visible.
Notes: Actual local UrbanEcho screenshot captured during Step 7 on 9 October 2026. All demonstration locations, recordings and calibration shown here are simulated. The application runs at http://localhost:8000/app. See CURRENT-STATUS.md and DEMO-WALKTHROUGH.md.

## Slide 4
The recording and reporting flow
04
Simulator
3 registered devices
FastAPI
audio upload
Worker calculates levels
Saved WAV + PostgreSQL / PostGIS
ESP32 + INMP441
Physical test pending
Thresholds
and incidents
Daily
summaries
Web application
Live alerts and daily reports
use saved server records.
Optional LAN HTTPS
prepared, disabled
Notes: Source: app/main.py, app/audio.py, app/processing.py, app/evaluation.py, app/daily.py, app/daily_jobs.py, app/device_api.py, compose.yaml and STEP6-VERIFICATION.md. WAV bytes live in a persistent volume. PostgreSQL/PostGIS stores metadata, measurements, incidents and summaries. Physical device uses the same upload contract through an optional private-LAN HTTPS listener. Listener is prepared but disabled.

## Slide 5
A repeatable noise incident demonstration
05
1
Normal and equal levels
No new incident
2
Above and sustained
One incident grows
3
Pause the sender
Stale, still unresolved
4
Three normal readings
Recovery resolves incident
5
Repeat an upload
Same saved recording
Demonstration inputs and calibration remain clearly marked SIMULATED.
Notes: Sources: SIMULATOR-VERIFICATION.md, scripts/verify-simulator.py and docs/step7/DEMO-WALKTHROUGH.md. The original runner verifies all three locations. Step 7 walkthrough demonstrates one selected excessive location while other locations stay normal. Threshold comparison uses unrounded values and strict greater-than. Stale status does not resolve an incident. Identical retries preserve recording identity. Screenshot is actual simulated local data.

## Slide 6
Daily reports show recorded coverage
06
Average of usable recorded time
Minimum and maximum levels
Eligible measurement count
Incident starts
Usable duration and coverage
Short samples represent only their recorded periods. Missing time never becomes a zero sound level.
Simulated dB SPL (Z). Real hardware starts uncalibrated.
Notes: Sources: app/daily.py, app/daily_jobs.py, README.md, DAILY-VERIFICATION.md and docs/step7/CURRENT-STATUS.md. Daily aggregation uses duration-weighted sound energy for compatible eligible measurements. Coverage is the union of usable intervals, not a count of all device-seconds. Local-day boundaries handle timezone and DST. Missing audio is not silence. This report is simulated and partial. Recalculation updates the stored summary identity.

## Slide 7
Verification evidence
07
Previously recorded: 9 October 2026 | Result
Backend automated checks | 382 passed
Frontend checks | 34 passed
Saved WAV checksums | 300 of 300 passed
Three-location demonstration | Two complete runs passed
NEW CHECKS IN STEP 7
5 focused tests passed. A fresh Workshop-only live demo passed, adding 30 recordings and 1 incident, then updating all three saved daily reports.
Simulated software evidence. Real-device and acoustic validation remain pending.
Notes: Source: STEP6-VERIFICATION.md, 9 October 2026. These are previously recorded checks. The Step 7 CURRENT-STATUS.md distinguishes new checks from this baseline.
Step 7 performed five targeted tests against disposable PostgreSQL/PostGIS, including both all-location and Workshop-only runs repeated twice. A fresh live demonstration passed on 9 October 2026 around 18:52–18:53 IST. It added 30 recordings and one resolved Workshop incident, preserved older records, and recalculated all three reports. The full 382-backend/34-frontend suites were not rerun for Step 7. See docs/step7/CURRENT-STATUS.md for detailed current checks and final results.

## Slide 8
ESP32 integration is prepared
08
FIRMWARE COMPILED
ESP32 + INMP441
C++ with ESP-IDF
1 second at 16 kHz
Mono PCM24 WAV uploads
Configurable capture/upload intervals
Private Wi-Fi settings, device credentials and the server address are still required.
INMP441 | ESP32
VDD / GND | 3.3 V / GND
SCK | GPIO 26
WS | GPIO 25
SD | GPIO 33
L/R | GND
Physical integration and acoustic validation pending
Notes: Source: STEP6-VERIFICATION.md, 9 October 2026. These are previously recorded checks. The Step 7 CURRENT-STATUS.md distinguishes new checks from this baseline.
Sources: firmware/esp32/README.md, docs/HARDWARE-INTEGRATION.md, firmware/esp32/main and user-confirmed wiring. ESP-WROOM-32-based board with INMP441. Exact carrier model/revision and flash capacity still need confirmation. ESP-IDF v5.4.3 target esp32 build/link passed. Physical board is on another computer. No claim of flashing, real captures, sound-pressure accuracy or calibrated monitoring.

## Slide 9
A residential community pilot
09
INITIAL OFFER
An 8-week pilot
1 community, 3 shared-area devices
Compare response time and complaint handling with a baseline.
Proposed pilot fee: ₹10,000–₹20,000, with hardware and calibration quoted separately.
FIRST 100 USERS
20 communities
5 recurring reviewers each
Manager interviews, one supervised pilot, then referrals.
A user reviews the product weekly for four weeks. Future independent use needs access controls.
Targets and prices are hypotheses to test with community managers.
Notes: Planning assumptions, not achieved sales or proven savings. Source: BUSINESS-CASE.md. Source: BUSINESS-CASE.md, sections 3–5. Pilot fee is an unvalidated price hypothesis. Users are facilities/security/committee reviewers, not residents, devices or paying organisations. Future site subscription hypothesis is ₹7,500–₹12,000 per community/month for up to three devices. No billing or multi-community service is implemented.

## Slide 10
Pilot cost assumptions
10
Item | Planning estimate | Basis
Complete device assembly | ₹1,800–₹3,000 each | Unquoted allowance
Local storage + backup | ₹8,000–₹14,000 once | Two 1 TB drives, allowance
Local hosting | ₹0 external fee | Existing PC, extras apply
Maintenance per site | ₹3,000–₹9,000/month | 4–12 h at ₹750/h
Future cloud example | US$37–78/month | 7–30 days of audio
Audio storage is a major design choice
Three devices recording continuously produce about 374 GB and 7.78 million WAV files per 30 days, before backups and database storage.
Notes: Source: BUSINESS-CASE.md and its dated sources. All planning amounts exclude unquoted acoustic calibration and certification. Continuous audio example: 48,044 bytes per one-second, 16 kHz PCM24 WAV × 86,400 × 30 × 3 = 373,590,144,000 bytes = 373.59 decimal GB, and 7,776,000 separate files. Excludes database, backups and filesystem metadata. No retention automation or cloud object-store migration has been implemented. Device allowance excludes site-dependent installation labour and calibration. Local primary and backup storage allowance is ₹8,000–₹14,000 for two 1 TB drives. Reference/calibration allowance is ₹10,000–₹25,000 per three-device pilot, unquoted. Bare retail reference: board ₹425 https://robocraze.com/products/esp32-development-board and microphone ₹148 https://robocraze.com/products/inmp441-mems-high-precision-omnidirectional-microphone-module-i2s (listing sold out). Future cloud calculation sources: https://www.digitalocean.com/pricing/droplets ($24 4 GiB/2-vCPU VM), https://docs.digitalocean.com/products/volumes/details/pricing/ ($0.10/GiB/month), https://www.backblaze.com/cloud-storage/pricing ($6.95/TB per 30 days). Observed 9 October 2026. Exact modeled totals $37.41 for seven-day retention and $77.80 for thirty-day retention. Cloud example includes a VM, provisioned audio volume and one logical audio backup, but excludes labour, taxes, currency conversion, DB backups and redundancy. No cloud service enabled.

## Slide 11
The next 12 months
11
Oct–Nov 2026
Step 8 acceptance, one real calibrated device and ten buyer interviews
Dec 2026–
Mar 2027
First pilot, then agreed retention, backup and viewer access controls
Apr–Jul 2027
Expand from 5 to 12 communities only after site and capacity checks
Aug–Sep 2027
Target 20 communities and 100 recurring reviewers if evidence supports it
Local simulated demonstration: ready
Physical monitoring: pending board test and calibration
Next milestone: real microphone, ESP32, UrbanEcho, incident alert and daily summary.
Notes: Proposed development and adoption plan, not committed delivery dates. Source: BUSINESS-CASE.md, CURRENT-STATUS.md and ACCEPTANCE-CHECKLIST.md. Gates depend on actual board tests, acoustic validation, consent/retention decisions, pilot evidence and reliable operation. Physical milestone: real microphone → ESP32 → UrbanEcho → incident alert → daily summary.